4 CAR TRAIN INSTRUCTIONS

Please check that you have all parts. (Located in attached bag)

- 8  ground stakes

- 4 wing bolts

- 1 pkg of asst. color clips (replacement)

- 1 black 3 point controller

Unfold display being careful not to stretch any attached wires.  There are 4 hinges on the display. On each car attach two small metal plates at hinges together by screwing wing bolt into metal plates to hold up display. Make sure bolt is on opposite side of the nut which is attached. Do not screw bolt into the side with the nut first.

Attach ground stakes by screwing them into the bottom provided slots. You may need an adjustable wrench.

Push ground stakes gently into the ground. You can do this with your foot and using a back and forth motion to inch each side gradually into the ground.

First, lay the cord set on the ground. (It looks better on the back side of the train).

- Plug the male end of the cord set into an extension cord.

- Plug the black 3 point controller into the first female plug of the cord set.

- Plug the upper part of the caboose into the next female plug on the cord set.

- Plug the Bear car into the next female plug.

- Plug the Candy Cane car into the next female plug.

- Then plug upper of the Engine car into the last female plug on the cord set.

- All of the train should be lighting except for the wheels.

- Starting at the back caboose wheels, Plug the male plugs from the wheels into the plugs on the controller. Each wheel is marked Green 1, Red 2 and Yellow 3. Match these numbers.

- Continuing to each car match the numbers. 1 to 1, 2 to 2, and 3 to 3.

- At the Engine front you will have 3 female plugs. The smoke from the top will plug into these three female plugs. Each smoke it labeled.

*** If you plug any of these into the controller and the light does not come on, for example, you plug up Green 1 to Green 1 and the lights do not come on, you need to turn that plug around. Some controllers have a polarity issue (only black controllers). IF the polarity is crossed it will not light. So by turning the prongs around, it will line up the polarity and the lights will come on.  We have also placed a dot on the controller plug and a dot on the decoration plug. If you line these dots up, then it will keep the polarity straight.

For the best look, straighten clips. Also, if you live in an area with lots of rain or snow, you may want to take extra precaution to cover your controllers. See our website for ideas on how to protect your controller.